## Slide 1
Digital Logic Design
Lecture 06
Copyrights: Dr Syed Zulqadar Hassan

## Slide 2: Boolean Algebra
Variable
Complement
Notes: Variable: A variable is a symbol usually an uppercase letter used to represent a logical quantity.
A variable can have a 0 or 1 value.
Complement: A complement is the inverse of a variable and is indicated by a bar over the variable.
Complement of variable X is X*
If X = 0 then X*= 1 and if X = 1 then X*= 0
Literal: A Literal is a variable or the complement of a variable. X and X* are literals

## Slide 3: Boolean Addition & Multiplication
Boolean Addition performed by OR gate
Sum Term describes Boolean Addition
Boolean Multiplication performed by AND gate
Product Term describes Boolean Multiplication

## Slide 4: Boolean Addition
Sum of literals
Sum term = 1 if any literal = 1
Sum term = 0 if all literals = 0
Notes: Sum term is described as sum of literals

## Slide 5: Boolean Multiplication
Product of literals
Product term = 1 if all literals = 1
Product term = 0 if any one literal = 0
Notes: Product term is described as product of literals

## Slide 6: Laws, Rules & Theorems of Boolean Algebra
Commutative Law
  for addition and multiplication
Associative Law
  for addition and multiplication
Distributive Law
Rules of Boolean Algebra
Demorgan’s Theorems

## Slide 7: Commutative Law
Commutative Law for Addition
A + B = B + A
Commutative Law for Multiplication
A.B = B.A
Notes: The basic laws of Boolean Algebra are the same as ordinary algebra and hold true for any number of variables

## Slide 8: Associative Law
Associative Law for Addition
A + (B + C) = (A + B) + C
Notes: The sum term B OR C Ored with A is the same as sum term A OR B Ored with C

## Slide 9: Associative Law
Associative Law for Multiplication
A.(B.C) = (A.B).C
Notes: The product term BC Anded with A is the same as AB Anded with C

## Slide 10: Distributive Law
A.(B + C) = A.B + A.C

## Slide 11: Rules of Boolean Algebra
A + 0 = A
A + 1 = 1
A.0 = 0
A.1 = A
A + A = A
A + = 1
A.A = A
A. = 0
= A
A + A.B = A
A + = A + B
(A+B).(A+C)
= A+B.C
Notes: A+A*B = A(B+1)+A*B using rule 2
=AB+A+A*B
=A+AB+A*B
= A+B
(A+B)(A+C) = A+AC+AB+BC
=A+BC

## Slide 12: Demorgan’s Theorems
First Theorem
Second Theorem
Notes: Demorgan’s First Theorem states: The complement of a product of variables is equal to the sum of the complements of the variables.
Demorgan;s Second Theorem states: The complement of sum of variables is equal to the product of the complements of the variables

## Slide 13: Demorgan’s Theorems
Any number of variables
Combination of variables
Notes: Demorgan’s Theorems can be applied to expressions having any number of variables
Demorgan’s Theorem can be applied to a combination of other variables

## Slide 14: Boolean Analysis of Logic Circuits
Boolean Algebra provides concise way to represent operation of a logic circuit
Complete function of a logic circuit can be determined by evaluating the Boolean expression using different input combinations
Notes: Boolean algebra provides a concise way to represent the operation of a logic circuit.
The complete function of the logic circuit can be determined by evaluating the Boolean expression using different input combinations.

## Slide 15: Boolean Analysis of Logic Circuits
From the expression, the output is a 1 if variable D = 1 and =1
=1 if AB=1 or C=0

## Slide 16: Boolean Analysis of Logic Circuits
Inputs |  |  |  | Output | Inputs |  |  |  | Output
A | B | C | D | F | A | B | C | D | F
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1

## Slide 17: Simplification using Boolean Algebra
AB + A(B+C) + B(B+C)
= AB + AB + AC + BB +BC
= AB + AC + B + BC
= AB + AC + B
= B + AC

## Slide 18: Simplified Circuit

## Slide 19: Standard forms of Boolean Expressions
Sum-of-Products form
Product-of-Sums form
Notes: Sum-of-Product (SOP) form: When two or more product terms are summed by Boolean addition, the result is a Sum-of-Product or SOP expression
Product-of-Sum (POS) form: When two or more sum terms are multiplied by Boolean multiplication, the result is a Product-of-Sum or POS expression
The Domain of an SOP and POS expression is the set of variables contained in the expression, both complemented and un-complemented.
A SOP and POS expression can have a single variable term such as A
A SOP and POS expression can not have a term of more than one variable having an over bar extending over the entire term.

## Slide 20: Standard forms of Boolean Expressions
Sum-of-Products form
AB + ABC
ABC + CDE +
Product-of-Sums form

## Slide 21: Implementation of SOP expression

## Slide 22: Implementation of POS expression

## Slide 23: Conversion of general expression to SOP form
Notes: Any logical expression can be converted into SOP form by applying techniques of Boolean Algebra

## Slide 24: Examples
Boolean Analysis of Circuit
Evaluating Boolean Expression
Representing results in a Truth Table
Simplification of Boolean Expression into SOP or POS form
Representing results in a Truth Table
Verifying two expressions through truth tables

## Slide 25: Analysis of Logic Circuits Example 1
Notes: Consider the logic circuit comprising of NOT gates, AND gates, NAND gate and NOR gate.
The circuit can be represented by a Boolean Expression
Let us define the Boolean expression that represents the Logic circuit.
Starting from the left hand side of the circuit
Output of NOT gate 1 is B*
Output of NOT gate 2 is A*
Output of two input AND gate 3 is AB*
Output of two input AND gate 4 is CD
Output of three input NAND gate 5 is (A*B*CD)*
Output of two input NOR gate 6 is (AB*+(A*B*CD)*)*

## Slide 26: Evaluating Boolean Expression
The expression
Assume and
Expression
Conditions for output = 1 X=0 & Y=0
Since X=0 when A=0 or B=1
Since
Y=0 when A=0, B=0, C=1 and D=1
Notes: Now consider the expression which has two terms
The term AB* and the term (A*B*CD)*
Assume that the term AB* is represented by literal X
Also assume that the term (A*B*CD)*is represented by the literal Y
Thus the expression is now represented as (X+Y)*
For which condition does the expression output a 1?
The expression shows that a NOR operation is being performed between terms X and Y.
Therefore when terms X and Y are both 0s only then the output is a 1.
The term X=AB* is 0 when literal A is 0 or literal B* is zero or B is 1.
The term Y=(A*B*CD)* is 0 when the term A*B*CD =1 the bar has been removed.
The term A*B*CD is 1 when literals A*=1, B*=1, C=1 and D=1
Or when A=0, B=0, C=1 and D=1

## Slide 27: Evaluating Boolean Expression & Truth Table
Conditions for o/p =1
A=0, B=0, C=1 & D=1
Input |  |  |  | Output
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Notes: Conditions for output =1 are
For the term AB* A=0 OR B=1
For the term (A*B*CD)* A=0 AND B=0 AND C=1 AND D=1
For both terms A has to be 0 otherwise the output is not equal to 1
B has to be 0 otherwise the second term is equal to 1 and the output 0
Similarly C and D variables have to be equal to 1s otherwise the second term is equal to 1 and the output 0
The truth table describes the function of the logic circuit and the expression where all outputs are equal to 0 except for the input combination of A=0, B=0, C=1 & D=1

## Slide 28: Simplifying Boolean Expression
Simplifying by applying Demorgan’s theorem
=
Notes: Let us verify the analysis of the Logic Circuit by simplifying the original Boolean expression representing the Logic Circuit and obtaining the truth table of the simplifies expression.
The two truth tables should be identical
The expression is simplified to (AB*)* ANDed with (A*B*CD)** by applying Demorgan’s 2nd theorem
Applying Demorgan’s 1st theorem and Rule No. 9 to the two terms results in (A*OR B**) ANDed with (A*B*CD)
The term (A* OR B**) simplifies to (A* OR B)
Applying the Distributive law the expression simplifies to A*B*CD
The conditions A=0, B=0, C=1, D=1 are identical to the original expression that was analysed.

## Slide 29: Truth Table of Simplified expression
Input |  |  |  | Output
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Notes: The truth table representing the function represented by the simplified expression is identical to the function represented by the truth table prepared earlier as a result of analysing the Boolean expression.

## Slide 30: Simplified Logic Circuit

## Slide 31: Simplified Logic Circuit
Simplified expression is in SOP form
Simplified circuit

## Slide 32: Second Example
Evaluating Boolean Expression
Representing results in a Truth Table
Simplification of Boolean Expression results in POS form and requires 3 variables instead of the original 4
Representing results in a Truth Table
Verifying two expressions through truth tables

## Slide 33: Analysis of Logic Circuits Example 2
Notes: Consider the logic circuit implemented using NOT gates, AND gate, OR gate and NAND gate.
The circuit can be represented by a Boolean Expression.
Let us define the Boolean expression representing the logic circuit.
Starting from the left hand side of the circuit
Output of NOT gate 1 is A*
Output of NOT gate 2 is C*
Output of three input AND gate 4 is A*BC*
Output of two input OR gate 5 is C*+D
Output of two input NAND gate 6 is ((A*BC*)(C*+D))*

## Slide 34: Evaluating Boolean Expression
The expression
Assume and
Expression
Conditions for output = 1 X=0 OR Y=0
Since
X=0 when A=1,B=0 or C=1
Since
Y=0 when C=1 and D=0
Notes: Now consider the expression which has two terms
The term A*BC* and the term C*+D
Assume that the term A*BC* is represented by literal X
Also assume that the term C*+D is represented by the literal Y
Thus the expression is now represented as (XY)*
For which condition does the expression output a 1?
The expression shows that a NAND operation is being performed between terms X and Y.
Therefore when term X OR the term Y is 0, the output is a 1.
The term X=A*BC* is 0 when literal A*is 0 or A=1, literal B is zero or literal C*=0 or C=1.
The term Y=C*+D is 0 when literals C*=0 and D=0
Or when C=1 and D=0

## Slide 35: Evaluating Boolean Expression & Truth Table
Conditions for o/p =1
(A=1,B=0 OR C=1) OR (C=1 AND D=0)
Input |  |  |  | Output
A | B | C | D | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Conditions for output =1 are
For the term A*BC* A=1 OR B=0 OR C=1
For the term C*+D C=1 AND D=0
The truth table outputs corresponding to the input conditions A=1, B=0 OR C=1 are marked as 1s
The truth table outputs corresponding to the input conditions C=1 AND D=0 are also marked as 1s

## Slide 36: Rewriting the Truth Table
Conditions for o/p =1
(A=1,B=0 OR C=1) OR (C=1 AND D=0)
Input |  |  | Output
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Notes: The 4-variable truth table shows that for all input combinations of variables A, B, C and D the output only depends on the inputs A, B and C. D does not play any role in the function output.
For example for the input combination A=0, B=1, C=1 the output is 1 if D=0 or D=1. Similar is the case for other inputs.
Thus a simpler 3 variable K-Map can represent the same function as the 4 variable K-map.

## Slide 37: Simplifying Boolean Expression
Simplifying by applying Demorgan’s theorem
Notes: Let us verify the analysis of the Logic Circuit by simplifying the original Boolean expression representing the Logic Circuit and obtaining the truth table of the simplifies expression.
The two truth tables should be identical
The expression is simplified to (A*BC*)* + (C*+D)* by applying Demorgan’s 1st theorem
Applying Demorgan’s 1st and 2nd theorems to the two terms respectively results in (A**+B*+C**) + (C**D*)
The expression simplifies to (A+B*+C) + CD*
Which simplifies to A+B*+C

## Slide 38: Truth Table of Simplified expression
Input |  |  | Output
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Notes: The truth table representing the function represented by the simplified expression is identical to the function represented by the truth table prepared earlier as a result of analysing the Boolean expression.

## Slide 39: Simplified Logic Circuit

## Slide 40: Simplified Logic Circuit
Simplified expression is in POS form representing a single Sum term
Simplified circuit

## Slide 41
THE END