## Slide 1: Digital Logic and Design
Dr. Syed Zulqadar Hassan
Lecture No. 09

## Slide 2: Recap
Karnaugh Maps
Mapping Standard SOP expressions
Mapping Non-Standard SOP expressions
Simplification of K-maps
Don’t care states

## Slide 3: Functions having multiple outputs
Ckt receives a BCD number input
Displays decimal number 0 to 9 on a single digit 7-segment display
Ckt receives two 2-bit numbers A and B
Sets one of three outputs to >, =, or <

## Slide 4: 7-Segment Display
Notes: 7-Segment display is shaped like the number 8
It has 7-segments that can be lit in different combinations to display any digit between 0 to 9.
The 7-segments are identified by segment numbers a, b, c, d, e, f and g.
The three horizontal segments starting from the top are a, g and f respectively
The two vertical segments on the right side are segments b and c
The two vertical segments on the left side are segments f and e
To display the numbers 0 to 9 different set of segments are turned on
0 a, b, c, d, e, f
1 b, c
2 a, b, d, e, g
3 a, b, c, d, g
4 b, c, f, g
5 a, c, d, f, g
6 a, c, d, e, f, g
7 a, b, c
8 a, b, c, d, e, f, g
9 a, b, c, d, f, g
The segment a, for example is turned on when numbers 0, 2, 3, 5, 6, 7 and 8 are displayed
The segment d, for example is turned on when the numbers 0, 2, 3, 5, 6 and 8 re displayed.
Similarly different sets of segments are selected to display different digits.
The 7-segment display circuit basically can be considered to be 7 different circuits having 4 inputs and 1 output
The 4-bit input of the circuit accepts BCD numbers and the output controls a single segment.
Before implementing the 7 circuits, function tables for each of the 7 circuits have to be prepared.

## Slide 5: Function Table for Segment ‘a’
Inputs |  |  |  | Output
A | B | C | D | a
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
Inputs |  |  |  | Output
A | B | C | D | a
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 6: Function Table for Segment ‘b’
Inputs |  |  |  | Output
A | B | C | D | b
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
Inputs |  |  |  | Output
A | B | C | D | b
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 7: Function Table for Segment ‘c’
Inputs |  |  |  | Output
A | B | C | D | c
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
Inputs |  |  |  | Output
A | B | C | D | c
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 8: Function Table for Segment ‘d’
Inputs |  |  |  | Output
A | B | C | D | d
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A | B | C | D | d
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 9: Function Table for Segment ‘e’
Inputs |  |  |  | Output
A | B | C | D | e
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A | B | C | D | e
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 10: Function Table for Segment ‘f’
Inputs |  |  |  | Output
A | B | C | D | f
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A | B | C | D | f
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 11: Function Table for Segment ‘g’
Inputs |  |  |  | Output
A | B | C | D | g
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A | B | C | D | g
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | X
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | X
1 | 1 | 1 | 1 | X

## Slide 12: Karnaugh Map for Segment ‘a’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 1 | 1
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 13: Karnaugh Map for Segment ‘b’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 1
01 | 1 | 0 | 1 | 0
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 14: Karnaugh Map for Segment ‘c’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 0
01 | 1 | 1 | 1 | 1
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 15: Karnaugh Map for Segment ‘d’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 1
01 | 0 | 1 | 0 | 1
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 16: Karnaugh Map for Segment ‘e’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 0 | 0 | 0 | 1
11 | x | x | x | x
10 | 1 | 0 | x | x

## Slide 17: Karnaugh Map for Segment ‘f’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 1 | 1 | 0 | 1
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 18: Karnaugh Map for Segment ‘g’
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 1
01 | 1 | 1 | 0 | 1
11 | x | x | x | x
10 | 1 | 1 | x | x

## Slide 19: 7-Segment Circuit

## Slide 20: Comparator Circuit
Inputs two 2-bit binary numbers A and B
Has three outputs
A>B
A=B
A<B

## Slide 21: Function Table for A>B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A>B
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A>B
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0
Notes: The function table for the output A>B represents the output of the circuit output logic line representing A>B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A>B line is set to 1 when A>B.
Thus for input combinations of A and B that is 01 00, 10 00, 10 01, 11 00, 11 01 and 11 10 the output A>B is 1

## Slide 22: Function Table for A=B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A=B
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A=B
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Notes: The function table for the output A=B represents the output of the circuit logic line representing A=B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A=B line is set to 1 when A=B.
Thus for input combinations of A and B that is 00 00, 01 01, 10 10 and 11 11 the output A=B is 1

## Slide 23: Function Table for A<B
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A<B
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
Inputs |  |  |  | Output
A1 | A0 | B1 | B0 | A<B
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Notes: The function table for the output A<B represents the output of the circuit logic line representing A<B for 16 combinations of the 2-bit numbers A and B.
The input numbers A and B are represented by A1A0 and B1B0 columns of the function table
Output A<B line is set to 1 when A<B.
Thus for input combinations of A and B that is 00 01, 00 10, 00 11, 01 10, 01 11 and 10 11 the output A<B is 1

## Slide 24: Karnaugh Map for A>B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 1 | 0 | 0 | 0
11 | 1 | 1 | 0 | 1
10 | 1 | 1 | 0 | 0
Notes: Simplifying expression for A>B through a 4-variable K-map yields A1B1*+A0B1*B0*+A1A0B0*
Note that the left most column has binary values 00, 01, 11 and 10 representing A1A0
The top row has binary values 00, 01, 11 and 10 representing B1B0

## Slide 25: Karnaugh Map for A=B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 0 | 1 | 0 | 0
11 | 0 | 0 | 1 | 0
10 | 0 | 0 | 0 | 1
Notes: Simplifying expression for A=B through a 4-variable K-map yields A1*A0*B1*B0*+A1*A0B1*B0+A1A0B1B0+A1A0*B1B0*

## Slide 26: Karnaugh Map for A<B
A1A0/ B1B0 | 00 | 01 | 11 | 10
00 | 0 | 1 | 1 | 1
01 | 0 | 0 | 1 | 1
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 1 | 0
Notes: Simplifying expression for A<B through a 4-variable K-map yields A1*B1+A1*A0*B0+A0*B1B0

## Slide 27: Odd Prime Number Circuit
Circuit detects odd prime numbers for a 4-bit input number
Function represented by minterms
1, 3, 5, 7, 11, 12 and 13