## Slide 1
Digital Logic & Design
Lecture 10

## Slide 2: Combinational Logic
Implementation of SOP using AND-OR

## Slide 3: SOP Implementation
Notes: The diagram shows the general architecture of the SOP Implementation.
SOP expression is implemented by the AND-OR combination of gates.
The AND gates produce the product terms.
Outputs of all the AND gates are connected to a single multiple input OR gate for sum of products.
The product terms comprise of literals in their complemented form and un-complemented form which are implemented by NOT gates connected to the inputs of the AND gates.

## Slide 4: Design and Implementation of Digital Circuits
Function Table
Simplification of Expression
Implementation

## Slide 5: Adjacent 1s Detector Circuit
SOP Implementation
  Directly from function table
Simplified implementation
Implementation using NAND gates

## Slide 6: Adjacent 1s Detector Function
Input |  |  |  | Output | Input |  |  |  | Output
A | B | C | D | F | A | B | C | D | F
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: The Adjacent 1s detector circuit accepts a 4-bit binary input and generates a 1 output when it detects a combination of two adjacent 1s.
The function diagram shows the 16 possible input combinations and the corresponding outputs.
Thus for the input combinations 0011, 0110, 0111, 1011, 1100, 1101, 1110 and 1111 the output function is a 1.
The information provided by the function table can be directly implemented to form the Adjacent 1s Detector circuit
How many AND gates are required?
Eight gates to implement the 8 minterms.
How many OR gates are required?
A single eight input OR gate is required to sum all the eight product terms.
Some NOT gates are also required to implement complemented literals in some of the product terms.

## Slide 7: SOP Implementation
Notes: The SOP based implementation of the Adjacent 1s detector circuit is shown implemented directly from the function table.
This implementation uses maximum number of gates.
The total gate count is
one 8 input OR gate
eight 4 input AND gates
ten NOT gates
All together 19 gates are required.
The increased number of gates increases the cost, the size of the circuit, the power requirement and the propagation delay which is of the order of three gates.

## Slide 8: SOP Expression Simplification
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 0 | 0 | 1 | 0
Notes: An appropriate way to implement the Adjacent 1s detector circuit is to simplify the SOP boolean expression represented by the function table and then implement the circuit based on the simplified expression.
The function table information is directly mapped to a 4-variable K-map
The 1s are grouped together forming three product terms
AB, CD and BC

## Slide 9: SOP based Simplified Circuit
Notes: The simplified circuit is implemented using
three 2-input AND gates
And a single 3-input OR gate.
The total circuit count is 4 gates.
The cost of the circuit reduces
The size of the circuit reduces
The power requirement of the circuit reduces
And the propagation delay has reduced from three gate delay to two gate delay.

## Slide 10: NAND based Implementation
Notes: The simplified 4 gate circuit can be implemented using only NAND gates without a change in the total number of gates.
Bubbles representing NOT gates are placed at the output of the three AND gates. Converting the three AND gates to NAND gates.
To balance out the three NOT gates added at the outputs of the three AND gates. Three bubbles representing three NOT gates are also placed at the three inputs of the OR gate.
The Resulting OR gate symbol with three bubbles at the three inputs is an alternate symbol for a three input NAND gate.
The NAND based circuit is shown.

## Slide 11: XOR & XNOR Gates
XOR function
XNOR function

## Slide 12: XOR Gate
Notes: The XOR operation performs a comparison function.
An XOR operation detects dissimilar inputs.
The XOR gate can be implemented using a combination of NOT-AND-OR gates.
Since the function performed by the XOR gate is commonly used in digital circuits therefore XOR gates are available in Integrated circuit form which can be readily used instead of implementing a XOR circuit based on NOT-AND-OR combination of gates.

## Slide 13: XNOR Gate
Notes: The XNOR operation performs a comparison function.
An XNOR operation detects similar inputs.
The XNOR gate can also be implemented using a combination of NOT-AND-OR gates.
Since the function performed by the XNOR gate is commonly used in digital circuits therefore XNOR gates are available in Integrated circuit form which can be readily used instead of implementing a XNOR circuit based on NOT-AND-OR combination of gates.

## Slide 14: Combinational Functional Devices
Comparators
BCD to 7-Segment
Parity Generator Circuit

## Slide 15: Half & Full Adders
Half Adder
Full Adder

## Slide 16: Half & Full Adders
Notes: The block diagrams represent a Full-Adder and a Half-Adder.
A single bit binary adder circuit basically adds two bits and a carry bit, generated by the addition of the least significant bits. The output of the single bit adder circuit generates a sum bit and a carry bit.
An adder circuit that only has two bit input representing the two single bit numbers A and B and does not have the carry bit input from the least significant digit is regarded as a half-adder.
An adder circuit that has three inputs, two bits representing the two single bit numbers A and B, and the third bit represents the Carry in bit is regarded as a full-adder

## Slide 17: Half-Adder
Function Table
Expression
Logic Circuit

## Slide 18: Half-Adder Function Table
Input |  | Output | 
A | B | Sum | Carry Out
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 19: Half-Adder Circuit

## Slide 20: Full-Adder
Function Table
Expression
Logic Circuit

## Slide 21: Full-Adder Function Table
Input |  |  | Output | 
A | B | Carry In (C) | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 22: Sum Expression

## Slide 23: Carry Out Expression

## Slide 24: Full-Adder Circuit

## Slide 25: Full-Adder
Full-Adder = Half-Adder + Half-Adder

## Slide 26: Full-Adder based on Two Half-Adders

## Slide 27: Parallel Binary Adder
Multiple Single bit Full-Adder connected in Parallel

## Slide 28: 4-bit Parallel Adder